## Slide 1
CAP7001:
Data Communication and Networking
Unit-II
Transmission Media

## Slide 2: Transmission Media
Channel carrying information signals.
Moves bits across LANs.
Physical path transmitter to receiver.
Copper uses electrical signals.
Fiber uses light pulses.
Layer 1 physical component.

## Slide 3: Classification of Transmission Media
Guided (wired) transmission media.
Unguided (wireless) transmission media.

## Slide 4: Factors Affecting Media
Bandwidth sets data rate.
Transmission impairment degrades quality.
Impairments: attenuation, distortion, noise.
Interference: unwanted signal addition.
Medium, signal characteristics matter.

## Slide 5: Guided Media
Physical bounded transmission paths.
Types: Twisted Pair cables.
Coaxial cable: baseband, broadband.
Fiber optic: single, multimode.

## Slide 6: Twisted Pair
Two insulated copper wires.
Twisted spiral noise reduction.
Cheap, lightweight, easy install.
Frequency range 0–3.5 kHz.
More twists reduce interference.

## Slide 7: Types of Twisted Pair

## Slide 9: Coaxial Cable
Two parallel conductors coaxial.
Higher frequency than twisted.
Inner copper, outer mesh.
Dielectric separates conductors centrally.
Mesh shields against EMI (Electromagnetic interference)

## Slide 10: Coaxial: Baseband vs Broadband
Baseband: single high-speed signal.
Broadband: multiple signals simultaneously.
Application-specific selection required.
Different equipment, modulation schemes.

## Slide 11: Fiber Optics Cable
Transmits using light signals.
Fibers coated with protective plastics.
Immune to electromagnetic interference.
Faster than copper wiring.
Supports high data rates.

## Slide 12: Fiber: Core/Cladding/Jacket
Core: light transmission region.
Larger core transmits more light.
Cladding lowers refractive index.
Enables internal total reflection.
Jacket protects strength, shock.

## Slide 13
THANK YOU